Ομάδα: Δ15
Μαρίτσας Νικολαος	–	031
Μυτης Ιωαννης	–	031
Παπαδοπουλλος Μιχάλης	–	03114702

3.1.asm:
.include "m16def.inc"

;-------------------
; REGISTER ALIASING
.def cnt=r20
.def input=r22

;-------------------
; PROGRAM CODE
;-------------------

;-------------------
.MACRO CHECK
LOOP:
in input,PINB
andi input,0x01
cpi input,0x01
breq LOOP
rjmp @0
.ENDMACRO
;-------------------

;-------------------
; INITIALIZING STACK
SETUP_STACK:
ldi r24,low(RAMEND)
ldi r25,high(RAMEND)
out SPL,r24
out SPH,r25
;-------------------

INIT:
ser cnt	; cnt = 1..1
out DDRA,cnt	; initialize PORTA as OUTPUT
clr cnt	; cnt = 0
out DDRB,cnt	; initialize PORTB as INPUT

MAIN:
in input,PINB	; read INPUT
andi input,0x01 ; get LSB
sbrc input,0	; skip if input[0] (bit) is reset (=0)
rjmp MAIN	; if input[0] (bit) == 0 then goto MAIN

inc cnt	; cnt = 1
jmp LSB_2_MSB

CHANGE_FROM_MSB_2_LSB:
lsl cnt	; start from the second bit

LSB_2_MSB:
out PORTA,cnt	;
rcall WAIT	; wait for 500ms
cpi cnt,0x80	; if 0b1000 0000 => last bit
breq CHANGE_FROM_LSB_2_MSB	; change direction
lsl cnt	; else, cntt << 1

CHECK LSB_2_MSB

CHANGE_FROM_LSB_2_MSB:
lsr cnt	; start from the sixth bit

MSB_2_LSB:
out PORTA,cnt	;
rcall WAIT	; 500 ms
cpi cnt,0x01	; first bit => change direction
breq CHANGE_FROM_MSB_2_LSB
lsr cnt

CHECK MSB_2_LSB

;-------------------
WAIT:
ldi r24,low(500)
ldi r25,high(500)
rcall wait_msec
ret
;-------------------

wait_usec:
sbiw r24,1
nop
nop
nop
nop
brne wait_usec
ret

wait_msec:
push r24
push r25
ldi r24,low(998)
ldi r25,high(998)
rcall wait_usec
pop r25
pop r24
sbiw r24,1
brne wait_msec
ret

3.2.asm:
.include "m16def.inc"

.def scan=r20
.def num=r19	;has input number
.def temp=r18
.def f0=r17
.def f1=r16
.def f2=r15

ser temp	;set PORTA as output and PORTC as input
out DDRA,temp
clr temp
out DDRC,temp

clr f0
clr f1
clr f2
ldi scan,0b00000011
in num,PINC	;get number from PortC
mov temp,num	;save number to temp

;With the use of variable scan each loop we isolate pair AB,BC etc
;check if it equals to 11
;and if yes then f0 is 0 so continue with f1.
;if no scan is rotated left to check the next pair
;if bit 5 of scan is 0 then every pair is 0 so f0 = 1
main:
and num,scan
cp num,scan
breq check_f1
lsl scan
mov num,temp	;get the input number to num
sbrs scan,0x05	;if scan out of bounds f0 = 1
rjmp main
ldi f0,0x01
check_f1:
mov num,temp
andi num,0b00001111	;same as f0 checking if ABCD = 1111 or B'E' = 00
cpi num,0b00001111
breq set_f1
andi temp,0b0011000
cpi temp,0b00000000
brne check_f2
set_f1:
ldi f1,0x01
check_f2:
or f2,f1	;if f0 or f1 = 0x01 then f2 = 0x01
or f2,f0
lsl f2	;slide f2 once to the left and put f1 or f0 to the lsb respectively
or f2,f1
lsl f2
or f2,f0
out PORTA,f2	;output to PORTA

3.2.c:
#include <avr/io.h>

unsigned char x, A, B, C, D, E, f0, f1, f2;
int main()
{
DDRA = 0xFF;	//output
DDRC = 0x00;	//input
while(1)
{
x = PINC & 0x1F;
A = x & 0x01;
B = (x & 0x02) >> 1;
C = (x & 0x04) >> 2;
D = (x & 0x08) >> 3;
E = (x & 0x10) >> 4;
f0 = !( (A & B) | (B & C) | (C & D) | (D & E) );
f1 = ( (A & B & C & D) | ((!D) & (!E)) ) ;
f2 = f0 | f1;
f2 = f2 << 2;
f1 = f1 << 1;
PORTA = (f2 | f1 | f0) & 0x7;
};
return 0;
}

3.3.c:
#include <avr/io.h>

//check if a bit is set or not
int checkBit(unsigned char byte, int offset)
{
byte = byte >> offset;
return (byte && 0x01);	//return the value of the bit
}

unsigned char resetBit(unsigned char byte, int offset)
{
if (offset == 4){	//if there is no input, do nothing
return byte;
}
unsigned char mask = 0x01;	//reset the bit that is about to serve its purpose
mask = mask << offset;
mask = !mask;
byte = byte & mask;
return byte;
}

int rotateLeft(unsigned char byte)
{
if(byte == 0x80)	//if you are on the left edge, return 0x01 (the right edge)
return 0x01;
else
return (byte << 1);	//otherwise shift left
}

int rotateRight(unsigned char byte)
{
if(byte == 0x01)	//if you are on the right edge, return 0x80 (the left edge)
return 0x80;
else
return (byte >>1);	//otherwise shift left once
}

int main(void)
{
DDRB = 0xFF;	//PORT B : output
DDRD = 0x00;	//PORT D : input

unsigned char input, output, input_rec, flag;

PORTB = output = 0x01; //set PB0
input_rec = 0x00; //set input_rec = 0x00 cause no input has been recorded yet

while(1) {
input = PIND; //input from portD
//input_rec variable holds each input given in real time	input_rec = input_rec | input;
flag = 4;	//there are only SW0,SW1,SW2,SW3 so if flag = 4 no input has been given
for(int i = 3; i >= 0; i--) { //SW3 has higher priority
if(checkBit(input_rec, I)) { //check if input bit is 1
flag = i;	//if it is 1 indeed, flag holds its position and then break
break;
}
}

//(input has been given) && (input_rec bit is set) && (input bit is reset)
//only when push button is unpushed changes take place

if(flag != 4 && checkBit(input_rec, flag) && checkBit(input, flag) == 0)
{
input_rec = resetBit(input_rec, flag);
//reset input_rec bit which is about to serve its purpose
switch (flag)
{
case 3:	output = 0x01;	//set PB0
break;
case 2:	output = 0x80;	//set PB7
break;
case 1:	output = rotateRight(output);
break;
case 0:	output = rotateLeft(output);
break;
}
PORTB = output;
}
}
return 0;
}